## Slide 1: SMART CHAIR CDR
Rudy Ramjas - EE
Mackenson Jean - EE
Annavay Kean - CpE
Thien Nguyen - CpE

## Slide 2: Goals & Objectives
Help user to become more mindful of posture habits.
Provide feedback based on measured data.
Target audience: middle-class office workers.
Methodology: Center of Gravity

## Slide 3: Specification Requirements
The application should remind the user to get up after specified time interval.
The application should provide feedback on the user’s posture.
The device should update the sensor input readings at a specified interval.
The device should pair with a phone app.
Sensor array should be able to load an average American citizen.
Physical method of notifying user to correct posture will be implemented.

## Slide 4: Overview Diagram

## Slide 5: Roles
Task | Primary | Secondary | Status
Wireless Communication | Thien | Annavay | proto
Database Development | Annavay | Thien | proto
Mobile Application | Annavay | Thien | Proto
Microcontroller | Rudy | Mackenson | Ordered
Power Supply | Mackenson | Rudy | proto
Rechargeable Battery | Mackenson | Rudy | Received
Force Sensor Integration | Rudy | Thien | proto
Vibration Module | Rudy | Thien | Received
User Interface | Annavay | Thien | In development
PCB Design | Mackenson | Rudy | 2nd iteration

## Slide 6: Microcontroller Selection
MCU | F280049PMSR | ATMEGA 2560-16AU | PIC24FJ1024GA606-I/PT | MSP430FR2311IPW16R | ATSAMA5D21C-CUR
Manufacturer | Texas Instruments | Atmel | Microchip Technology | Texas Instruments | Microchip Technology
Program Memory (kB) | 256 | 256 | 1024 | 3.75 | 160
Data Memory (kB) | 100 | 8 | 32 | 8 | 128
Clock Frequency (MHz) | 100 | 16 | 32 | 16 | 500
GPIO | 26 | 86 | 53 | 11 | 128
Supply Voltage Range | 1.2 - 1.3V | 1.8V – 5.5V | 2 - 3.6V | 1.8V -3.6V | 1.2V
Size L x W (cm) | .072 x .072 | 1.6 x 1.6 | .07 x .07 | .05 x .04 | 1.4 x 1.4
Price (USD) | $10.81 | $12.20 | $4.41 | $1.62 | $6.71

## Slide 7: MCU Dev board

## Slide 8: Power supply
The system will be powered by an AC to DC adapter.
It will be operated by a voltage range from 12V to 3.3V.
The PCB will be using power 24 hours and keep it running under all conditions.
Back up power will provide to the chair by a 9V battery to allows the circuit running after it is disconnected to the wall.
The battery will take over when the main power source is unplugged.

## Slide 9: Battery Supply
9V Rating
Lithium ion composition
Rechargeable
Less Expensive
Easily substitutable

## Slide 10: Schematic Overview

## Slide 11: PCB Power Section

## Slide 12: Overall PCB

## Slide 13: FSR Selection
 | Tekscan A502 | Tekscan A301 | SEN-09376 | FSR-406
Price per unit | $23.24 | $12.18 | $11.25 | $12.99
Surface Area(in2) | 4 | 0.375(diam) | 3.0625 | 2.25
Response time(µs) | ≤ 5 | ≤ 5 | ≤ 5 | ≤ 5
Load range(N) | 44kN max | 444N max | * | 100N max
Drive voltage(V) | Variable | Variable | * | *
Amplifier circuit | Multiple | Multiple | Volt. Div. | Multiple

## Slide 14: FSR Selection
Tighter tolerance: < 3%
Multiple integration methods
  Voltage Divider
Engineering support (Manufacturer)

## Slide 15: Proximity Sensor

## Slide 16: Vibrate Module

## Slide 17: Software Design
  Wireless Communication
  NoSQL Database
  Application Framework

## Slide 18: Wireless Modules
Bluetooth | Wi-Fi
Shorter Range | Longer Range
Close proximity | Remote Location
Direct Connections | Online Connection
Lower Power | Higher Power

## Slide 19: Flowchart Diagram

## Slide 20: Bluetooth Specification
Hardware Features | Software Features
-80 dBm sensitivity | PIO: low-disconnect & high-connect
+4 dBm RF transmit power | Rising Pulse will disconnect
Low Power 1.8 V Operation | Auto-connect on last device
PIO Control | Pair Last Device as Default
UART Interface | PINCODE: 0000 / 1234

## Slide 21: Wi-Fi Specification
Hardware Features | Software Features
CPU: Tensilla L 106 32-bit | Security: WPA / WPA2
Integrated Memory (SRAM) | Encryption: WEP/TKIP/AES
SPI External Flash | Firmware: OTA Network
RF 2.4 GHz Receive/Transmit | SDK: Supports Cloud Server
Adjustable Power Mode | Network Protocol: TCP/UDP/HTTP

## Slide 22: Wi-Fi Module
ESP8266
Breadboard testing
Surface mount
Antenna RF optimization

## Slide 23: ESP8266 Schematic
Main Aspects
Power Supply
Power-on sequence and reset
Flash
Crystal oscillator
RF
External resistor
UART

## Slide 24: ESP8266 Pros and Cons
Pros
Compatibility with IDE
Multiple GPIO pins
Powerful capabilities
Cons
Difficult to start working
Requires multiple libraries

## Slide 25: Wireless Communication
Sensor data
Wi-Fi Transmission
Send data through cloud
Database Receive data

## Slide 26: Purpose of Application
To allow the user to view posture data.
To provide feedback on posture data to the user.
To allow the user to alter settings.

## Slide 27: Application Design
Technologies Used:
  Firebase serves as the back-end. It provides user authentication, password hashing and salting, and provides a portal to manage the NoSQL database.
    Benefits: Free to use.
    Drawback: Less flexibility of design.
  Flutter serves as the front-end framework. Flutter is a framework developed by Google to speed up user interface development via widgets. Uses the Dart language.
    Benefits: Hot reload
    Drawback: Nested code requires planning

## Slide 28: NoSQL Database Design
Provides support for offline data persistence.
Each data entry contains the center of gravity on the left-to-right axis and the front-to-back axis and the timestamp.
  This is subject to change during the process of integrating the legitimate sensor data into the software.

## Slide 29: User Interface Design

## Slide 30: User Interface Design

## Slide 31: Application Completion Status
Complete:
  Firebase authentication
  Firebase database (including read/write)
  Basic Layout
  Basic navigation
Pending:
  Settings / User Preferences
  Posture data represented in graphical format
  Recommend Stretches/Yoga poses
  Swipe navigation
  Color Theming

## Slide 32: PROGRESS GRAPH
Chart: 
| Research | Low level software implementation | High Level software Implementation | PCB | Sensor integration | Total
 | 0.9 | 0.25 | 0.56 | 0.52 | 0.5 | 0.546

## Slide 33: BUDGET SHEET
Item | Description | Quantity | Cost | Total | Estimated Cost
Tekscan A301 | round force sensors - 4 pk | 1 | $53.60 | $53.60 | $150.00
Tekscan A502 | Larg square force sensors - 4 pk | 1 | $108.25 | $108.25 | 
556-ATMEGA2560-16AU | Microcontroller | 3 | $12.20 | $36.60 | $40.00
Chair | Office chair, cloth, rolling | 2 | 0 | 0 | $75.00
Eleego Mega 2560 R3 | ATmega Dev board | 1 | $13.99 | $13.99 | $16.00
HC-SR04 | ultrasonic proximity sensor | 1 | 0 | 0 | $10.00
Mircrochip ATMega2560 | microcontroller samples from OEM | 5 | 0 | 0 | -
Final Paper | printing and binding via ... | 1 | $27.98 | $27.98 | $30.00
System Enclosure | Housing for PCB |  |  |  | 
PCB surface components | PCB resistors, caps, etc. | Multiple |  | 34.17 | $50.00
Firebase | Backend manager | 1 | - | - | -
ESP8266 |  |  |  |  | 
Total |  |  |  | $272.33 | $800.00

## Slide 34: Implementation Challenges
Software-Hardware Integration
  Proper data transmission
  Formatting data
Foam of chair (Sensors)
  Reduce thickness of foam
  Add barrier between sensors and foam

## Slide 35: Q&A